## Slide 1: Network Devices

## Slide 2: Classification
Connecting devices can be classified by considering the layer at which they operate
  Layer 1 Physical
    Repeaters
    Hubs
  Layer 2 Data Link
    Switches
    Bridges
  Layer 3 Network
    Routers

## Slide 3: Hub
A hub (or repeater), being at layer 1, has no knowledge of frames or packets; it only knows bits.
It forwards every bit to all ports, i.e. it has not any filtering capability.
Obsoleted by switches.

## Slide 4: Switch (bridge)
A switch, being a 2-layer device, “knows” frames, but not packets.
It has a switching table and uses MAC addresses to find the port to which forward the input frame, i.e. it has filtering capabilities at layer 2
  The table is normally built automatically (learning switch)
It is used to interconnect devices belonging to the same LAN

## Slide 5: Learning switch (bridge)
M
M
M
M

## Slide 6: Router
A router, being a 3 layer device, knows packets.
It has a routing table with network addresses
The routing table can be manually set (static rules) or dynamically built
It is used to connect one LAN to Internet (as in ADSL “routers”), or multiple independent LANs (building an inter-net), or different Internet parts
It operates on network addresses. It changes destination MAC addresses of packets that traverse the router.