## Slide 1: TCP-Tuning
Advanced, not required for the exam

## Slide 2: RTT impact
The RTT determines TCP performance in 2 ways
  First, the Tx rate is inversely proportional to RTT for the same W.
    Tx=W/RTT
    This means that in order to achieve the same Tx rate, if the RTT is doubled you must double W.
      Let us arbitrarily assume RTT=25ms as a benchmark;
      RTT=200ms from Italy to US West cost; W must be 8 times larger than in the benchmark case to achieve the same rate;
      RTT=600ms on a GEO sat; W must be 24 times larger!
    In fact, you need W=500 segments of 1500B each, to get 10 Mbit/s on a GEO sat (RTT=600ms) instead of 21 on the benchmark.
  Second, to «add insult to injury» the growth of the cwnd in time is RTT paced, i.e. inversely proportional to it.
    Although larger cwnd are required, the cwnd growth is slowed-down!

## Slide 3: TCP Tuning
There are some (actually, >50 in Linux!) TCP related parameters that can be configured to improve performance
To cope with large W
  Large windows (cwnd and rwnd) require large Tx and Rx TCP buffers; you likely need to enlarge the defaults
  The TCP Window Scale Option must set on (default in Linux)
    With rwnd=64KiB, max Tx speed is limited to 2.6 Mbit/s on a Europe-US West coast link and to just 873.8 kbit/s on a GEO
  The SACK option must set on (default in Linux)
    SACK is useful to cope with multiple losses on the same window; the larger the window, the more likely this event;
  The Timestamps Options must be set on (default in Linux)
    It improves RTT estimates.
To cope with slow cwnd dynamic
  Use an experimental (i.e. non RFC compliant) congestion control instead of NewReno
    There are ten available in Linux
    Cubic is the default in Linux and is NOT RFC compliant (but performs much better than NewReno)
    Hybla has been designed to cope with long RTTs; is available in Linux (note that Hybla also would require packet pacing, which is not included in Linux)

## Slide 4: On the spot TCP «tuning» in Linux
To check all TCP settings
  sysctl -a|grep ipv4.tcp|more
To temporarily enlarge TCP buffers
  Type: sysctl -w net.ipv4.tcp_rmem='4096 65536 8388608'
    TCP Autotuning setting. "The first value tells the kernel the minimum receive buffer for each TCP connection, and this buffer is always allocated to a TCP socket, even under high pressure on the system. ... The second value specified tells the kernel the default receive buffer allocated for each TCP socket. This value overrides the /proc/sys/net/core/rmem_default value used by other protocols. ... The third and last value specified in this variable specifies the maximum receive buffer that can be allocated for a TCP socket."
  Type: sysctl -w net.ipv4.tcp_wmem='4096 65536 8388608'
    TCP Autotuning setting. "This variable takes 3 different values which holds information on how much TCP sendbuffer memory space each TCP socket has to use. Every TCP socket has this much buffer space to use before the buffer is filled up. Each of the three values are used under different conditions. ... The first value in this variable tells the minimum TCP send buffer space available for a single TCP socket. ... The second value in the variable tells us the default buffer space allowed for a single TCP socket to use. ... The third value tells the kernel the maximum TCP send buffer space."
  Type:sysctl -w net.ipv4.route.flush=1
    This will ensure that immediately subsequent connections use these values.
To temporarily set on the TCP Window Scale, the SACK and the Timestamp options (all on by default in Linux)
  Type: sysctl -w net.ipv4.tcp_window_scaling =1
  Type: sysctl -w net.ipv4.tcp_sack =1
  Type: sysctl -w net.ipv4.tcp_timestamps = 1
To temporarily set an experimental (i.e. non RFC compliant) congestion control (Cubic is default in Linux)
  Type: sysctl -w net.ipv4.tcp_congestion_control=cubic (or hybla)

## Slide 5: Permanent TCP «tuning» in Linux
To make default changes permanent, add (as a root) the following lines to /etc/sysctl.conf :
  net.ipv4.tcp_rmem=4096 65536 8388608
  net.ipv4.tcp_wmem=4096 65536 8388608
  net.ipv4.tcp_window_scaling =1
  net.ipv4.tcp_timestamps = 1
  net.ipv4.tcp_sack = 1
  net.ipv4.tcp_congestion_control=cubic
  Or
  net.ipv4.tcp_congestion_control=Hybla
A reboot is needed for changes to take effect, or you can attempt to reload sysctl settings (as a root) with sysctl -p.

## Slide 6: Other sysctl «tuning» in Linux
To see all sysctl values
  Type: sysctl –a|more
To restrict the output to the sysctl subset containing the word tcp
  Type: sysctl –a|grep tcp|more
You can change temporarily or permanently the default values as seen for TCP tuning
Remember to set on routing on routers!
  Uncomment the line below in /etc/sysctl.conf:
    net.ipv4.ip_forward = 1
Useful Links
  https://www.nas.nasa.gov/hecc/support/kb/optional-advanced-tuning-for-linux_138.html
  http://fasterdata.es.net/host-tuning/

## Slide 7: APE “Tuning”
Yes, it may be funny too; but with TCP you tuning you do not risk to be fined!

## Slide 8: Extreme “Tuning”
Any comments?